Compiler

- Syntax similar to AMORAL,but entirely interpreted.
- Split up into procedures w/parameters.
- Replace all strings with constants holding addresses.
- Replace all constants (various formats) with addresses.
- Replace all variables with addresses. $ is used to prefix locals.
- Centralised storaged for constants & strings to minimise duplication.
- Compile code for lall procedures.
- Align to byte page.
Memory Usage

Runtime / binary	Header (64 bytes): / Jump to initial code (+0) / Jump to opcode executor (+4) / Address of first procedure (+8) / Load address (+10) / Start of Variable space to erase (+12) / End of Variable space to erase (+14) / Constants
	Runtime code interpreter, standard routines.
Libraries	Library code written in 6502 assembler. Uses a FORTH type link but offset forward so can be simply battened together which has name, param count, address of 1st parameter (if > 1), as usual last parameter is passed in R.
Compiler / Generated / Binary	Generated code from compiling MTL
	ASCIIZ Strings.
	System variables (e.g. free.memory) starts on page boundary.
	Variables containing constant values.
Free / Memory	Variable space (erased to zero on start up)
	Free memory space.

Runtime

Opcodes	Instructions
0000-8FFF	LDR STR ADD SUB MUL DIV AND ORR XOR, the operand is a variable index into the variable space (e.g. doubled and added to the variable base address which is on a page boundary). Opcode is 12 bit unsigned.
9000-BFFF	BRA BEQ BPL conditional branch which conditional on the current value. Opcode is 12 bit signed.
C000-FFFF	CALL a 6502 routine at (lower 12 bits x 4). Routines executing runtime will start with a call to the runtime executor (stored in vectors)